## Slide 1: Kalman Filter Simplified
Jorge Jurado-Garcia

## Slide 2: Goal and Breakdown
Goal: Have an intuitive understanding of why and how Kalman Filter is used.
  Understand its disadvantages and advantages
  Comparison with common filter(s): Moving average filter(s)
  NO COMPLEX MATH!

## Slide 3: What is uncertainty and noise?
Noise: unwanted interference that degrades a signal. Makes the signal harder to understand and predict
Uncertainty : Confidence of an event, or model
Two Main types:
    Measurement Uncertainty
    Estimated Uncertainty
    Error Uncertainty

## Slide 4: Examples in Fiancé and Engineering
Small Price Movements and corrections is noise
  Difficult to determine actual trends or actual changes
Any Models or forecasting WILL HAVE SOME TYPE OF UNCERTAINTY.
Object Trackers:
  Noise(s): Thermal Noise, ADC Conversions, Variance in acceleration
  Due to this noises any THEORETICAL MODEL will be wrong!

## Slide 5: Kalman Filter to the Rescue
Estimation Algorithm that provides Quick, accurate, and precise estimates of a system with the presence of uncertainty due to noise.
Can Predict Future Events
Self alliterative – No selective windowing
Fast Processing with large amounts of data

## Slide 6: Simplified Flowchart

## Slide 7: Three Key Questions
(A)
(B)
(C)
(D)
If Kalman Gain is close to 0, then we are more uncertain about the measured values due to measurement error
If Kalman Gain is close 1, then we believe are measurements are accurate and have no measurement error

## Slide 8: 1-D Example
Noisy Coefficient |  | Initial Estimate |  | Initial Error in Estimate | Initial MEA | Error in MEA
0.1 |  | 90 |  | 10,000.10 | 31 | 13.69
Time | Measurement | True Value | Error in Measurement | Kalman Gain | Error in Estimate | Estimate
-1 |  |  |  |  | 10000.10 | 90.00
0 | 31 | 34.9 | 13.69 | 0.9986 | 13.77 | 31.08
1 | 39 | 35.1 | 13.69 | 0.5015 | 6.97 | 35.05
2 | 32 | 34.85 | 13.69 | 0.3372 | 4.72 | 34.02
3 | 37 | 35.01 | 13.69 | 0.2562 | 3.61 | 34.79
4 | 34 | 34.99 | 13.69 | 0.2086 | 2.96 | 34.62
5 | 36 | 34.5 | 13.69 | 0.1776 | 2.53 | 34.87
6 | 35 | 35.3 | 13.69 | 0.1560 | 2.24 | 34.89
7 | 31 | 35.2 | 13.69 | 0.1404 | 2.02 | 34.34
8 | 39 | 35.6 | 13.69 | 0.1287 | 1.86 | 34.94
9 | 38 | 34.6 | 13.69 | 0.1197 | 1.74 | 35.31
10 | 33 | 34.1 | 13.69 | 0.1127 | 1.64 | 35.05
Chart: Comparison of Measured, True Value, and Estimated Value
| -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Measurement | 31 | 39 | 32 | 37 | 34 | 36 | 35 | 31 | 39 | 38 | 33
True Value | 34.9 | 35.1 | 34.85 | 35.01 | 34.99 | 34.5 | 35.3 | 35.2 | 35.6 | 34.6 | 34.1
Estimate | 90 | 31.0807 | 35.0521 | 34.0229 | 34.7857 | 34.6218 | 34.8665 | 34.8874 | 34.3416 | 34.9411 | 35.3073 | 35.0472

## Slide 9: Comparison to Moving Average Filters

## Slide 10: Disadvantage(s) of Model
In rapid change situations, Kalman Filter has a slow reaction speed
For non-linear systems Kalman Filter becomes more complex
  Therefore, Kalman Filter are mostly only used for linear systems
The more inputs into your model the more computational expensive

## Slide 11: Interactive Python Kalman Filter
Go to Python Script